## Slide 1: Metabolic Model-based Tools for Optimizing Chinese Hamster Ovary Bioprocesses Michael Betenbaugh Johns Hopkins University Seongkyu Yoon University of Massachusetts Lowell
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 2: Introduction
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland
This comprehensive tool combines three functions that utilize the genome-scale model developed for Chinese Hamster Ovary (CHO) cell (https://doi.org/10.1016/j.cels.2016.10.020)
Stand-alone .exe version created using MATLAB
1st function: Amino acid level prediction tool for CHO cell culture
2nd function: Media optimization tool for CHO culture
3rd function: Clone analysis tool for CHO cell line

## Slide 3: Amino Acid Level Prediction Tool for Chinese Hamster Ovary Cell Culture Michael Betenbaugh Johns Hopkins University
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 4: Introduction
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland
Objective for this tool:
Facilitate CHO bioprocesses by providing predictive capabilities on key nutrient levels for improved process monitoring and control
Use easy-to-measure inputs (cell density) to predict hard-to-measure properties (amino acid levels)
Used Software and Algorithms:
Stand-alone .exe version created using MATLAB
COBRA Toolbox (https://opencobra.github.io/cobratoolbox/latest/index.html#), under GNU General Public License version 3.0
Developed “ENM” algorithm (doi.org/10.1038/s41540-019-0103-6)

## Slide 5: Amino acid level prediction algorithm
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Viable Cell Desnity (VCD) measurements and growth prediction precede AA prediction
Growth behavior predicted by equation fitting/two-point extrapolation
Essential AA level estimated by CHO model and ENM approach (published, doi.org/10.1038/s41540-019-0103-6)
Switchable Kalman filter mitigates negative impact of input error

## Slide 6: Graphical User Interface (GUI)
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
A Graphical User Interface (GUI) was made for AA level predictions
Input and initialize
Prediction parameters setting
Output
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 7: Input Data and Model
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland
Files to be loaded into the GUI:
Genome-scale model input into this GUI in .mat (MATLAB) format
Input data (cell density, initial amino acid levels) in Excel format
Required input data: 1st line: Culture time; 2nd line: VCD measurement; 1st column: initial amino acid levels
For record and comparison: Amino acid level measurements

## Slide 8: Prediction Method Selection and Parameter Setting
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Growth estimation method can be selected:
  Fitting, Logistic growth equation (needs >3 VCD measurements)
  Fitting, Exponential growth equation (needs >3 VCD measurements)
  Two-point extrapolation method (needs > 2 VCD measurements)
  Default method (run all fitting methods and select the fitting that gives the largest R2 value; two-point extrapolation if R2 < 95% )
Users can choose to predict future level after how many hours
Kalman filter can be turned on/off; estimated measurement and prediction errors are needed for input
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 9: Output from the GUI
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
1st output: Growth curve fitting results (with plot) and parameters; with cell density estimated for one future time point
2nd output: As many as 12 amino acid levels predicted (with plot) if no measurement is provided for the given time points, as well as levels predicted for a future time point
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 10: Output from the GUI
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
3rd output: A new Excel file containing previous inputs as well as predictions of future time points; this file can be used as input for next time point prediction
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 11: Output from the GUI
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
These outputs can be used as an estimation of future states in the CHO cell culture (i.e. bioreactors in CHO bioprocesses)
Future states can be used as guidance to design process control strategies
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 12: Media Optimization and Clone Analysis Tools Seongkyu Yoon University of Massachusetts Lowell
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 13: Introduction
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland
Objective for this tool:
Suggest target nutrients for optimizing culture media for CHO cells based on genome-scale model predictions of maximal growth rate/protein productivity
Suggest key metabolic pathways which affect the maximal growth/productivity as targets for cell line engineering
Used Software and Algorithms:
Stand-alone .exe version created using MATLAB
COBRA Toolbox (https://opencobra.github.io/cobratoolbox/latest/index.html#), under GNU General Public License version 3.0

## Slide 14: Experiments required for GUI
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Cell culture experiments
To calculate the specific consumption/production rates used as model constraints (model inputs)
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 15: Experiments required for GUI
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Data collection template (mg/mL, mmol/L)
Specific rates template (mmol/gDW hr)
 | D0 | D1 | D2 | D3 | … | D14 | Basal media | Feed media
Glucose |  |  |  |  |  |  |  | 
Glutamate |  |  |  |  |  |  |  | 
NH4 |  |  |  |  |  |  |  | 
lactate |  |  |  |  |  |  |  | 
Alanine |  |  |  |  |  |  |  | 
Serine |  |  |  |  |  |  |  | 
Cell growth |  |  |  |  |  |  |  | 
IgG |  |  |  |  |  |  |  | 
Specific rates calculation Equations
 | Batch1 | Batch 2 | Batch 3
Glucose |  |  | 
Glutamate |  |  | 
NH4 |  |  | 
lactate |  |  | 
Alanine |  |  | 
Serine |  |  | 
Cell growth |  |  | 
IgG |  |  | 
GUI (MATLAB)
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland

## Slide 16: GUI
Confidential
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
University of Maryland
Media optimization
Cell line analysis
Input: Measured metabolite fluxes + target nutrient to optimize
Output: Expected max growth or productivity change
Input: Measured metabolite fluxes + target gene to knockout
Output: Expected max growth or productivity change

## Slide 17: GUI - Media optimization
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
A Graphical User Interface (GUI) was made for media optimization (mainly for feed media）
GUI window
Network of Cell lines
Specify constraint inputs
Objective function
Targeted nutrient to optimize
Run simulation
Click 1

## Slide 18: Media optimization GUI - examples
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Optimize cell growth during exponential phase
Optimize IgG productivity during stationary phase
His can be used for future design
Pro can be used for future design

## Slide 19: GUI – Cell line analysis
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Main GUI window
Network of Cell lines
Specify constraint inputs
Pathway selection (sub GUI)
Gene knockout
Objective function
Run simulation
Click 1
Click 2
Click 3
Click 4
A Graphical User Interface (GUI) was made for clone analysis (mainly for gene knockout/knock in simulation）

## Slide 20: Clone analysis GUI – examples
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Sub GUI window
Gene lists:
  Gene symbol
  Gene description

## Slide 21: Clone analysis GUI - examples
Johns Hopkins University
Clemson University
University of Delaware
University of Massachusetts Lowell
Confidential
Knockout
Gene: 100758414
Knockout
Gene: 100764163