## Slide 1: Maximizing Yields of rAAV and Elucidating the Role of Media Components Through Design and Optimization of AMBIC.293 Media
David McNally (MassBiologics/UML), Seongkyu Yoon (UML), Mike Betenbaugh/Michael Bevan (JHU), Kelvin Lee (UD)

## Slide 2: UML and JHU Update (Media)
Original AMBIC media preparation
  Adding back the additives to the media
Cell banking
Reconstituted AMBIC media preparation based on the Plackett-Burman design
  Adding back the Non-Essential amino acids (NEAAs) and additives to the media
Next steps

## Slide 3: Original AMBIC Media Preparation
AMBIC media without 5 additives (Cacl2, CaPanto, FeEDTA, EDTA, and NaCl)
Adding back 5 additives
original media
Osmo adjustment
Adding back 5 additives to the media (Cacl2, CaPanto, FeEDTA, EDTA, and NaCl)
Osmolality adjustment by adding NaCl
Filtration of the media (original media)
300 mOsm/kg
260 mOsm/kg

## Slide 4: Original AMBIC Media Preparation
AMBIC media without 5 additives (Cacl2, CaPanto, FeEDTA, EDTA, and NaCl)
Adding back 5 additives
original media
Using for the cell thaw and passaging until recovery
Osmo adjustment
300 mOsm/kg
260 mOsm/kg
Using for the cell thaw and passaging until recovery
P3D4:
Viability: 93%
VCD: 5E6 cells/mL
P3D4:
Viability: 92%
VCD: 3E6 cells/mL

## Slide 5: Cell banking
AMBIC media without 5 additives (Cacl2, CaPanto, FeEDTA, EDTA, and NaCl)
Adding back 5 additives
original media
Using for the cell thaw and passaging until recovery
Osmo adjustment
300 mOsm/kg
260 mOsm/kg
Using for the cell thaw and passaging until recovery
P3D4:
Viability: 93%
VCD: 5E6 cells/mL
P3D4:
Viability: 92%
VCD: 3E6 cells/mL
Today is P4D4
Sending some vials to JHU and UD
Cell banking

## Slide 6: Plackett-Burman Design Review
Std Order | Run Order | PtType | Blocks | Arginine | Asparagine | Serine | Aspartic acid | Valine | cell growth | genome titer | Transduction efficiency | Empty/full Capsid ratio | DNA integrity
1 | 1 | 1 | 1 | 5 | 2 | 10 | 2 | 1 |  |  |  |  | 
2 | 2 | 1 | 1 | 5 | 8 | 2 | 10 | 1 |  |  |  |  | 
3 | 3 | 1 | 1 | 1 | 8 | 10 | 2 | 4 |  |  |  |  | 
4 | 4 | 1 | 1 | 5 | 2 | 10 | 10 | 1 |  |  |  |  | 
5 | 5 | 1 | 1 | 3 | 5 | 6 | 6 | 2.5 |  |  |  |  | 
6 | 6 | 1 | 1 | 5 | 8 | 2 | 10 | 4 |  |  |  |  | 
7 | 7 | 1 | 1 | 5 | 8 | 10 | 2 | 4 |  |  |  |  | 
8 | 8 | 1 | 1 | 1 | 8 | 10 | 10 | 1 |  |  |  |  | 
9 | 9 | 1 | 1 | 1 | 2 | 10 | 10 | 4 |  |  |  |  | 
10 | 10 | 1 | 1 | 3 | 5 | 6 | 6 | 2.5 |  |  |  |  | 
11 | 11 | 1 | 1 | 1 | 2 | 2 | 10 | 4 |  |  |  |  | 
12 | 12 | 1 | 1 | 5 | 2 | 2 | 2 | 4 |  |  |  |  | 
13 | 13 | 1 | 1 | 1 | 8 | 2 | 2 | 1 |  |  |  |  | 
14 | 14 | 1 | 1 | 1 | 2 | 2 | 2 | 1 |  |  |  |  | 
15 | 15 | 1 | 1 | 3 | 5 | 6 | 6 | 2.5 |  |  |  |  | 
Input: NEAA conc
Output (response): cell growth and productivity, transduction efficiency, capsid empty/full ratio, DNA integrity
Range: 2X Formulation; 0.5X Formulation
Plackett-Burman design
5 factors
12 runs + 3 center points runs 15 total runs
1 block

## Slide 7: Reconstituted AMBIC Media Preparation (NEAA Example)
AMBIC media without 5 additives (Cacl2, CaPanto, FeEDTA, EDTA, and NaCl) and 5 NEAAs (Arg, Asn, Asp, Ser, Val)
Adding back 5 additives
Adding back 5 NEAAs
Reconstituted media
13 different media formulations with their distinct NEAAs concentrations based on the DOE
Using Sigma-Aldrich amino acid standards (Arg, Asp, Asn, Ser, and Val).​
MilliQ water for dissolving the amino acids.
0.22 µm filtration of amino acid solutions.
Adding the filtered amino acid solutions and additives to the deleted media (Cacl2, CaPanto, FeEDTA, EDTA, and NaCl)
Osmolality adjustment by adding NaCl
Filtration of the media post reconstitution with amino acids and additives

## Slide 8: Confirmation of Amino Acid Concentration in Reconstituted Media
  Checking the consistency between the 13 prepared reconstituted media formulations and Plackett-Burman design prior to execution
13 different media formulations with their distinct NEAAs concentrations based on the prepared DOE
Reconstituted media
NEAAs measurement

## Slide 9: Workflow for DoE Study
Switching from the original media to the reconstituted media
original media
cell thaw and passaging until recovery
P3 or P4?
reconstituted media
3 passages in each of 13 reconstituted media
Daily cell counts
Transfection of AMBIC HEK293 cells [one shake flask for each condition]
qPCR (Taqman)
3 times freeze/thaw for cell lysis
Cell harvest on day 3 post-transfection
Transduction efficiency
capsid empty/full ratio
DNA integrity

## Slide 10: Next steps
Recover HEK293 ATCC cell bank, ensure all sites have the same cells before DOE (UML)
Osmo measurements and formulation of all DOE designs (UML and JHU)
Begin DoE screens for essential amino acid deleted media (UML and JHU)
  Finalized good range for AA differences: Osmo, literature or screening
Mass photometry development for full/total capsid analysis (JHU)

## Slide 11: UDel Updates
Progress of Full:Empty enrichment process
Full:Empty measurement by HPLC

## Slide 12: First gen F/E AEX separation
Empty removal
41% of capsids
9% of VGs
Full elution
59% of capsids
91% of VGs
Good
Process achieved full capsid enrichment with high yield (~91%)
Bad
Removed less than half of total capsids loaded (est. 15% full load material)
Co-elution of full capsids with aggregates and impurities (HCPs)
Buffer A – 20 mM BTP, 2 mM MgCl2, pH 9
Buffer B – 20 mM BTP, 2 mM MgCl2, 200 mM NaAc, pH 9
Flow rate – 5 mL/min
Resin – Capto Q
Column – TRICORN 5/100
System – Akta AVANT

## Slide 13: Optimized AAV9 F/E Separation
Three step process developed for improved impurity clearance (HCPs, aggregates)
3.2-fold enrichment in full capsids with >50% VG processing recovery (based on AAVX Octet and qPCR data)
Empty capsid removal
Full capsid collection
Impurity removal

## Slide 14: Scale up processing completed
After processing and buffer exchange, approx. 5E13 capsids were recovered at 1E13 capsids per mL (5 mL)
Bulk material was measured to be approx. 50% full based on HPLC peak integration
Pre-AEX
Post-AEX
empty
empty
full
full
partial

## Slide 15
HPLC method development for F/E measurement
Binary Pump
A: 20 mM bis-tris propane, pH 9.0, 2 mM MgCl2
B: 20 mM bis-tris propane + 250 mM sodium acetate trihydrate, pH 9.0, 2 mM MgCl2
0% B
9% B
30% B
Optimized for serotype 9 by lowering concentration of bis-tris propane and salt and adjusting step gradients and isocratic hold

## Slide 16
Accurate and reproducible full-to-empty capsid ratios can be measured with Agilent Bio SAX strong anion exchange columns
Efficient, simple, small volume, excellent linearity and reproducibility
Relative peak height or area~ F/E ratio
Best method to integrate peaks?
(1)
HPLC method development for F/E measurement
(1) Liau, B. Agilent Applications, 2022‌